## Slide 1: Traffic Signal Construction and Inspection in Pennsylvania
Chapter 4:
Materials and Products
Notes: Welcome to Module 4 of the Traf Signal Constr & Inspect in PA e-learning course. In this module, we will discuss a variety of materials and products.

## Slide 2: General
106.01 GENERAL—Use material complying with the requirements of these specifications. At the pre-construction conference, submit a list of material to be sampled and tested by the Contractor and a list of material to be sampled and tested by the Department.

## Slide 3: Acceptance of Traffic Signal Materials
Acceptance of the following material on construction projects by certification is based on their appropriate Publication 408 (Standard Specifications) reference
Item | Publication 408 Reference
Traffic Signal Support, Mast Arm | Section 951.2
Traffic Signal Support, Strain Pole | Section 951.2
Traffic Signal Support, Pedestal | Section 951.2
Controller Assembly | Section 951.2
Traffic Signal Systems and Communication | Section 953.2
Electrical Distribution System | Section 954.2
Signal Heads | Section 955.2
Detectors | Section 956.2
Traffic Signals (Manufactured Materials) | Section 1104
Temporary Traffic Control Signals | Section 1124
Manual Section 4.1

## Slide 4: Acceptance of Traffic Signal Materials
All traffic signal materials should be listed on Form CS-201
The Districts review and check the form, except for the structural support poles
In accordance with Department specifications, the engineer may accept certification of materials in lieu of inspection and testing

## Slide 5: Traffic Signal Product Approvals
The Bureau of Maintenance and Operations (BOMO) issues a Certificate of Approval (COA) to manufacturers authorizing the sale of specific electrically-operated traffic signal equipment
Contractors are responsible to tabulate a list of the proposed equipment
Manual Section 4.2

## Slide 6: Traffic Signal Product Approvals
BOMO also approves standard loadings for traffic signal supports, but shop drawings are submitted and design calculations are required for non-standard loadings

## Slide 7: Traffic Signal Product Approvals
Three copies of
  Warranties
  Guarantees
  instruction manuals
  wiring diagrams
  field wiring diagrams
  parts lists

## Slide 8: Traffic Signal Product Approvals
  One copy of each should be retained as follows
  Department file
  Municipal file
  Retained in the controller cabinet
  Publication 35, Bulletin 15 information

## Slide 9: Bulletin 15 Approval Process
Bulletin 15 Approval Process
  Product Evaluation Application Form (CS-4170)

## Slide 10: Bulletin 15 Approval Process
Bulletin 15 Approval Process
  The following entities are eligible to apply for Bulletin 15 approval:
    Manufacturers
    Steel Epoxy Coaters or Galvanizers
    Wood Treaters
    Steel, Aluminum or Timber Fabricators
    Machine Shops
    Paint Shops
    Precast/Prestressed Concrete Producers
    Cement Plants or Terminals
    Pozzolan Providers
    Bituminous Terminals or Refineries

## Slide 11: Bulletin 15 Approval Process
Bulletin 15 Listings
  Organized in the format of Publication 408, Specifications

## Slide 12: Bulletin 15 Approval Process
Bulletin 15
  Will indicate if a supplier is on a reduced Level of Certification
  Indicate by notation if a product has received either a Provisional Approval or a Conditional Approval

## Slide 13: Bulletin 15 Removal Actions
Bulletin 15 Removal Actions
  A manufacturer and/or product(s) may be removed from Bulletin 15
  Refer to manual for list of reasons

## Slide 14: Department Shop Drawing Approval
Department Shop Drawing Approval
  Shop drawings are required for all traffic signal supports on each project
  Department has a pre-approval process
  Only need to verify that loading meets contract requirements and matches pre-approved drawings

## Slide 15: Catalog Cut Sheets
General term for a few pages of specifications, instructions, dimensions, etc.
Generally shipped with the product
Generally specific enough to convey any information that might be needed to install or use the product
Manual Section 4.3

## Slide 16: Catalog Cut Sheets
Should include the following information:
  Manufacturer’s make and model number for each piece of equipment
  Quantity of items to be used
  Catalog Cuts may or may not require an Engineer’s seal
    The Department requires an engineering seal for Structural Support submissions
  Either the traffic signal unit or materials unit usually pre-approves the catalog cut sheets on either the CS-201 or directly on the cut sheets

## Slide 17: Proprietary Equipment Approvals
Occasionally, the Department receives requests from municipal officials to specify a particular brand of traffic signal equipment in the special provisions for a project
Attempt to use non-proprietary equipment
Will consider proprietary if in public interest
Manual Section 4.4

## Slide 18: Testing
Contractor is required to perform tests on various items during the construction of a traffic signal project
Documentation of some test results is required by the contractor, all other tests will have to be documented by the inspector
Following is a tabulation of required tests with references to the section of the specification requiring the test
Publication 408 Section | Test Performed
Sec. 1104 | Controller Assembly Shop Test.
Sec. 1104 | Traffic Signal Installation 30-Day Operating Test.
Sec. 952.3(a) | Malfunction Management Unit or Conflict Monitor Function Test.
Sec. 952.3(b) | Time Clock Evaluation.
Sec. 953.3(d) | 30-Day Systems and Communications Test.
Sec. 954.3(j) | Traffic Signal Circuits Test for Short Circuits, Unspecified Grounds, and Resistance to Earth Ground.
Sec. 956.3(a) | Loop Detector Leakage Resistance, Series Resistance, and Inductance Testing.
Sec. 956.3(a) | Earth’s Magnetic Flux Test and Magnetometer Detector Leakage and Series Resistance Test.
Sec. 956 3(a) | Magnetic Detector Leakage and Series Resistance Test.
Sec. 956.3(b) | Pedestrian Pushbuttons Evaluation and Pedestrian Phase Timing Test.
Sec. 953.3(k) | Traffic Signal Communications Test for Short Circuits, Unspecified Grounds, and Resistance to Ground.
Manual Section 4.5

## Slide 19: Rotational Capacity Test
Rotational Capacity Test
  AASHTO M-164 (ASTM A-325)
  A test, “that is intended to evaluate the presence of a lubricant, the efficiency of the lubricant, and the compatibility of assemblies as represented by the components selected for testing.”
  Rotational Capacity Test is included in Publication 19 as PTM 427

## Slide 20: High Strength Bolt Inspection Testing
High Strength Bolt Inspection Testing
  This method of test is in accordance with AASHTO M-164 (ASTM A-325), and AASHTO M-253 (ASTM A-490)
  The High Strength Bolt Inspection Test is included in Publication 19 as PTM 429.

## Slide 21: Bench Testing
Bench Testing
  “The critical evaluation of a new or repaired component, device, apparatus, etc., prior to installation to ensure that it is in perfect condition.”

## Slide 22: Bench Testing
Bench Testing
  Following bench tests may be performed:
    Tested for compatibility with all signal controller assemblies used by the Department
    BIU components in specified tolerances
    MMU components in specified tolerances

## Slide 23: Bench Testing
Bench Testing
  Continued:
    TYPE I or II Controller verified for full functionality and manufacturer’s claimed operation
    Loop amplifier verified for full functionality and manufacturer’s claimed operation
    TS-2 Card Rack Counting Loop Amplifier verified for full and manufacturer’s claimed operation
    Field Master Controller verified for full functionality and manufacturer’s claimed operation

## Slide 24: Field Testing
Field Testing
  Consist of installing the cabinet component in an actual traffic signal system for the specified testing period to monitor the following:
    Failures for the component
    Relative ease of use for the field personnel
    Overall build quality and expected lifecycle of the cabinet component

## Slide 25: Traffic Signal Specifications Sheet
PennDOT BOMO maintains a traffic signal specifications sheet for many commonly used traffic signal products
Manual Section 4.6

## Slide 26: Example
Example:
ITEM | Publication 408 Reference |  |  | Publication 148 Reference | Central Office Specification | National Reference | PennDOT Approval # Required | Active Product Approval Listing PennDOT Publication 35 (Bulletin 15)
 | Materials | Construction | Measurement and Payment | Standard Drawing |  |  |  | 
Traffic Signal Support – Mast Arm | 951.2,1104.01, 1104.02 | 951.3 | 951.4 | TC-8801 | Publication 149, Chapter 20 | AASHTO 2001 and MUTCD 2009 Edition | YES | 1104.02

## Slide 27: Item
Item: Traffic Signal Support – Mast Arm

## Slide 28: Publication 408, Materials
Publication 408, Materials: 951.2

## Slide 29: Publication 408, Materials
Publication 408, Materials: 1104.01

## Slide 30: Publication 408, Materials
Publication 408, Materials: 1104.02

## Slide 31: Publication 408, Construction
Publication 408, Construction: 951.3

## Slide 32: Publication 408, Measurement and Payment
Publication 408, Measurement and Payment: 951.4

## Slide 33: Publication 148, Standard Drawing
Publication 148, Standard Drawing: TC-8801

## Slide 34: Central Office Specification
Central Office Specification: Publication 149, Chapter 20

## Slide 35: National Reference
National Reference: AASHTO 2001 and MUTCD 2009 Edition
PennDOT Approval # Required: YES
  Approval number is required for this item, Traffic Signal Support – Mast Arm
  For traffic signal products in Publication 35 (Bulletin 15), the traffic division “Approval Certificate” number is used

## Slide 36: Active Product Approval Listing PennDOT Publication 35 (Bulletin 15)
Active Product Approval Listing PennDOT Publication 35 (Bulletin 15): 1104.02

## Slide 37: Are you Awake

## Slide 38: Common Electrical Materials
The following sections describe a variety of the commonly used electrical materials used on traffic signal projects
The list is not all-inclusive and additional materials may be used
This section of the course is intended to be self-paced
  Slides will not advance automatically
  Take time and review materials as desired/necessary
Manual Section 4.7

## Slide 39: Ground Wire
Ground Wire
  Description: Bare or insulated (green) copper wire, 8 AWG, conforming to ASTM B 3
  Use: Grounding wire for 120V AC circuits

## Slide 40: Ground Rod
Ground Rod
  Description: Copper-clad steel, UL listed
  Use: Grounding rod for 120V AC circuits

## Slide 41: Ground Rod Clamp
Ground Rod Clamp
  Description: Ground wire clamp.
  Use: Bronze clamp or exothermic weld for connection to grounding conductor.

## Slide 42: Conduit
Conduit
  Description: May be rigid steel or PVC
  Use: Houses electrical conductors.

## Slide 43: Signal Wire
Signal Wire
  Description: 14 AWG minimum, stranded conductors; conforming to IMSA Specification 19-1 or 20-1.
  Use: To provide electricity to equipment.

## Slide 44: Control Cable
Control Cable
  Description: Multi-conductor bundled cable with assorted stranded copper wires
  Use: Used to provide electrical energy

## Slide 45: Junction Boxes
Junction Boxes
  Description: Watertight boxes of various materials, gasketed lid held down with stainless steel screws
  Use: The junction box is used as an access to conduit and wire

## Slide 46: Terminal Blocks
Terminal Blocks
  Description: UL-listed with twelve sets minimum to two terminals suitable for the applicable wire size
  Use: For terminating wires/cables in signal pole or cabinet

## Slide 47: Loop Feeder Cable
Loop Feeder Cable
  Description: Polyethylene jacketed, shielded cable with two twisted No. 14 AWG wires and bare tinned copper drain wire or No. 14 AWG wires wrapped with mylar tape
  Use: Connects pairs of loop wires to controller, splice only at the junction box nearest the loop wires

## Slide 48: Loop Splice
Loop Splice
  Description: Two-piece plastic enclosure flooded with silicon grease
  Use: Used to connect loop feeder and loop wire (splice point)

## Slide 49: Loop Wire (XHHW/DUCT)
Loop Wire (XHHW/DUCT)
  Description: Stranded copper conductor, with crosslinked polyethylene insulation, No. 14 AWG wire
  Use: Used to detect vehicles

## Slide 50: Traffic Signal Specific Materials
The following sections describe a variety of the commonly used traffic signal specific materials used on traffic signal projects
The list is not all-inclusive and additional materials may be used
Manual Section 4.8

## Slide 51: Aluminum Sign
Aluminum Sign Mounting Framework
  Description: An aluminum assembly for mounting signs on a mast arm and spanwire installations
  Use: To attach signs to a mast arm or span wire

## Slide 52: Backplates
Backplates
  Description: Aluminum sheet powder-coated flat black louvered or black polycarbonate attached with stainless steel screws and washers with reflective sheeting along the edge
  Use: Shield around vehicle signal to provide a contrast to the background

## Slide 53: Eyebolt, Turnbuckle, Strandvise
Eyebolt, Turnbuckle, Strandvise
  Description: Hardware for attaching spanwire installations to strain poles
  Use: Used to hang the messenger cable (cable above signal heads

## Slide 54: 6-pair Interconnect Cable
6-pair Interconnect Cable
  Description: Shielded cable containing 6+ twisted pairs of No. 19 AWG wires
  Use: For communication between traffic signal controllers

## Slide 55: LED Modules (Vehicle & Ped)
LED Modules (Vehicle & Ped)
  Description: Light Emitting Diode (LED) Unit which replaces incandescent bulbs in signal heads and pedestrian heads
  Use: To illuminate vehicle and pedestrian signals
 | Section 1104 of Publication 408 indicates that the following must be Bulletin 15 approved: LED Vehicular and Pedestrian Signal Modules LED Countdown Pedestrian Signal Modules LED Lane-Use Traffic Control Signal Heads

## Slide 56: Messenger Cable
Messenger Cable
  Description: Bare steel cable comprised of seven strands of galvanized wire
  Use: Supports control cables, signal heads and signs on a spanwire installation

## Slide 57: Meter Base
Meter Base
  Description: Socket into which the power company’s meter is installed.
  Use: For power companies to meter power

## Slide 58: Pedestal (Pedestrian Signal)
Pedestal (Pedestrian Signal)
  Description: Galvanized steel pipe mounted on a cast aluminum or galvanized cast iron base
  Use: Freestanding pole for mounting of pedestrian signals and/or traffic signal indications

## Slide 59: Pedestrian Signal
Pedestrian Signal
  Description: Pole mounted signals. Aluminum powder-coated black or black polycarbonate with stainless steel hardware
  Use: To indicate walk/don’t walk pedestrian phases at marked crosswalks

## Slide 60: Pedestrian Signal Mount
Pedestrian Signal Mount
  Description: Swing open clam shell compartment
  Use: To connect pedestrian signal to pole, with wire terminals

## Slide 61: Preformed Loops
Preformed Loops
  Description: Four turns of No. 14 AWG XHHW or No. 16 AWG TFFN wire encased in either schedule 40 PVC or rubber hydraulic hose totally filled with sealant
  Use: Used to detect vehicles in thin, poor pavement or concrete bridge decks

## Slide 62: PTR Signs
PTR Signs
  Description: Flat black, painted, aluminum alloy case with part-time legend when lit
  Use: To indicate part time restrictions when turned on.

## Slide 63: Push Button
Push Button
  Description: A tamper and weatherproof assembly with pushbutton contacts, entirely insulated from the housing and buttons
  Use: For pedestrians to request the walk phase

## Slide 64: Riser Frames
Riser Frames
  Description: One piece welded construction for newer installations; two-piece bolt together for retro-fit
  Use: To raise the controller cabinet from the foundation 8

## Slide 65: Service Cabinet
Service Cabinet
  Description: Base mounted service cabinet with integral meter base
  Use: Used to provide fused electrical service

## Slide 66: Spanwire Hanger
Spanwire Hanger
  Description: A fitting of cast bronze that attaches to the messenger cable with two “U” bolts
  Use: To mount vehicle signal and signs on span wires

## Slide 67: Tether & Stabilizer Cable
Tether & Stabilizer Cable
  Description: One-quarter inch galvanized steel cable comprised of seven strands of galvanized wire
  Use: Attached at the bottom of equipment to stabilize and prevent wind movement

## Slide 68: Tether Clamp
Tether Clamp
  Description: Fitting on bottom of span mounted signal or sign constructed of 1½ inch galvanized steel pipe or galvanized metal conduit with plate welded on bottom, tether wire keeper bolted to plate
  Use: To attach tether cable to vehicle signals and signs

## Slide 69: 4.8 Traffic Signal Specific Materials
Tri-Stud Adaptors
  Description: Fitting of cast aluminum with steel insert, powder-coated as per spec
  Use: To mount signals and signs to plumbizer or span wire hanger

## Slide 70: Vehicle Signal Bracket (Adj.)
Vehicle Signal Bracket (Adj.)
  Extruded aluminum assembly that is adjustable
  Use: To mount vehicle signals and signs on a mast arm

## Slide 71: Vehicle Signal Visor
Vehicle Signal Visor
  Description: Aluminum powder-coated black or black polycarbonate open at bottom standard (tunnel)
  Use: On all signal heads to direct the illumination to the motorist

## Slide 72: Vehicle Signals
Vehicle Signals
  Description: Aluminum powder-coated black or black polycarbonate
  Use: To direct vehicles at intersections

## Slide 73: Traffic Signal Controller Materials
The following sections describe a variety of the commonly used traffic signal controller materials used on traffic signal projects
The list is not all-inclusive and additional materials may be used
Manual Section 4.9

## Slide 74: Controller Cabinet
Controller Cabinet
  Description: Ground mounted and pole mounted signal cabinets.
  Use: Houses the equipment to run the traffic signal

## Slide 75: Controller
Controller
  Description: NEMA or 170 controller unit
  Use: The brains of the traffic signal

## Slide 76: Conflict Monitor
Conflict Monitor
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: Monitors the green indications (vehicle) and walk indications (pedestrian) to ensure conflicting movements are not serviced at the same time

## Slide 77: Load Switch
Load Switch
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: Powers the signal and pedestrian indications in the field

## Slide 78: Flasher
Flasher
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: Powers the signal indications when in flash mode

## Slide 79: Detector Amplifier
Detector Amplifier
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: A device that is capable of detecting the changes in the electrical energy produced by a sensor

## Slide 80: Isolator (DC and AC)
Isolator (DC and AC)
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: Detects when a pedestrian pushes a button or when a train is approaching and puts a “call” into the controller

## Slide 81: Modem
Modem
  Description: NEMA or 170 as indicated in contract documents and Publication 408
  Use: Provides communications between traffic signals and/or to the central traffic signal operations office

## Slide 82: Relay (FTR)
Relay (FTR)
  Description: Model 430
  Use: Switches the power from the load switches (normal operation) to the flashers (flash operation)

## Slide 83: Preemption Interface (Cabinet)
Preemption Interface (Cabinet)
  Description: Several models acceptable for use
  Use: Detects an emergency vehicle (that is using a preemption emitter in their vehicle) and puts a “call” into the controller

## Slide 84: Preemption Detector (Field)
Preemption Detector (Field)
  Description: Several models acceptable for use
  Use: Detects an emergency vehicle (that is using a preemption emitter in their vehicle) which is recognized by the preemption interface in the cabinet

## Slide 85: GPS Time Sync Module
GPS Time Sync Module
  Description: Per Publication 408 Section 1104
  Use: To keep accurate time in the traffic signal controller

## Slide 86: Video & Radar Detection Device
Video & Radar Detection Device
  Description: Camera mounted to mast arm or luminaire arm
  Use: Alternative detection mode for vehicles

## Slide 87: Audible Pedestrian Signal
Audible Pedestrian Signal
  Description: Audio unit mounted near signal head and/or pushbutton.
  Use: Provides sight impaired pedestrians’ audible information regarding the pedestrian phases

## Slide 88: Battery Back-up System
Battery Back-up System
  Description: Uninterrupted Power Supply (UPS)
  Use: Provides power to the traffic signal when commercial power is out

## Slide 89: Chapter 4 Quiz

## Slide 90: Module 4 Completion
You have now completed Module 4, Materials and Products
To review any section in this module, use the “Outline” on the left
Up next is Module 5, Traffic Signal Construction
It is suggested that you complete Module 5 before proceeding to the additional modules

## Slide 91: Remaining Modules
The remaining modules include:
  Module 5: Traffic Signal Construction
  Module 6: Traffic Signal Inspection
Return to the PennDOT Technical Training Calendar to select Module 5