## Slide 1: Traffic Signal Construction and Inspection in Pennsylvania
Module 6:
Traffic Signal Inspection

## Slide 2: Introduction
Key PennDOT document for traffic signal inspection is Publication 669
Info in this section follows flow of Publication 669
Presentation includes some additional details
Manual Section 6.1

## Slide 3: Purpose of Publication 669
Purpose of Publication 669
  Intended to assist the Inspector (construction or HOP projects) in:
    recognizing the components of a traffic signal
    ensuring that all contract requirements are met in the traffic signal installation
    as a roadmap to the PennDOT traffic signal requirements

## Slide 4: Authorization for Inspection
Authorization for Inspection
  The work on traffic signal construction projects will be subject to the inspection of the representative or authorized assistants

## Slide 5: Responsibilities of the Inspector and District Traffic Unit
Responsibilities of the Inspector and District Traffic Unit
  Responsibilities of the inspector and District Traffic Unit are described in Sections 1.6 and 1.7, respectively

## Slide 6: General Inspection Principles
General Inspection Principles
  Important that adhere to the contract documents
  Deviation from the drawings should only be done after consultation with the District Signal Supervisor

## Slide 7: Submittals and Approvals
Submittals and Approvals
  Verify that the contractor completes and submits the CS-201

## Slide 8: Submittals and Approvals
Submittals and Approvals
  Typical materials requiring prior approval as specified in Section 1104.01 of Publication 408 are:
    Traffic Signal structural support (PennDOT approved shop drawing)
    Traffic Signal controllers
    Flasher units

## Slide 9: Submittals and Approvals
  Cont’d
    Signal (vehicular and pedestrian) and Light Emitting Diode (LED) modules
    Detector amplifiers and/or detection systems
    Preemption systems (if applicable)
    Pedestrian pushbuttons and Accessible Pedestrian Signals (APS) (if applicable)
    Electrically operated signs (if applicable)

## Slide 10: Submittals and Approvals
Submittals and Approvals
  Work with the contractor to submit the following:
    Three copies of the cabinet wiring diagram and manufacturer's timing plan for each controller assembly
    Three copies of warranties, guarantees, instruction manuals, wiring diagrams and parts lists

## Slide 11: Submittals and Approvals
  Cont’d:
    Two keys for each controller cabinet lock (Two for the Number 2 cabinet lock and two police keys)
    Shop drawings and calculations for approval for all traffic signal supports on the project

## Slide 12: Miscellaneous Requirements and Information
Verify that the contractor permanently marks the following materials with the manufacturer's name, serial number and model or part number:
  Controller Unit
  Conflict Monitor
  Flashers

## Slide 13: Miscellaneous Requirements and Information
Cont’d
  Relays
  Load Switches
  Time-base Units, including GPS units
  Detector Amplifiers

## Slide 14: Miscellaneous Requirements and Information
Cont’d
  Detector Power Supplies
  Detection Systems & equipment
  Interfaces
  Modems
  Emergency Vehicle Preemption Units
  Uninterrupted Power Supply (UPS) System

## Slide 15: Miscellaneous Requirements and Information
Verify that the contractor maintains removed controller assemblies as a unit and stores the material at the project site in a secure location
    refer to Publication 408, Section 1104.01

## Slide 16: Miscellaneous Requirements and Information
Contact the District Signal Supervisor at least 7 calendar days before marking pole locations so it may be determined if a Traffic Unit Representative should be present

## Slide 17: Miscellaneous Requirements and Information
  Verify that, after the new installation is operational, the contractor removes all:
    existing traffic signal supports (including those with traffic signals)
    flashing warning devices
    lane control signs and signal equipment, unless otherwise directed
  All equipment removed shall be returned to the municipal traffic signal owner

## Slide 18: Miscellaneous Requirements and Information
Document any damage to the equipment before its removal
Unless otherwise noted, underground conduit, conductors, and detectors not interfering with new construction can be left in place

## Slide 19: Miscellaneous Requirements and Information
If there are any questions concerning deviation from Publications 408 and 148, the special provisions and the contract plans, it is critical that the Inspector contact the Inspector In-Charge and the District Signal Supervisor

## Slide 20: Miscellaneous Requirements and Information
Existing traffic signals are to remain and continue their current operation until the new signal is operable, absent any provisions to the contrary
If any vegetation is obstructing the visibility of traffic signal indications (vehicular and pedestrian) or signs, work with the contractor to request and obtain approval to remove the obstructions

## Slide 21: Miscellaneous Requirements and Information
Verify that the contractor identifies possible utility conflicts early
Verify that conflicting signs are bagged immediately after the signal is turned on
Obtain from the contractor the name and telephone number of the person to be notified in the event of failures or malfunctions during the guarantee period

## Slide 22: Electrical Service Connections
Electrical Service Type A (Wood Poles)
  Verify the Contractor coordinates with the utility company for location of the service feed
  Verify that wood utility poles are 30’ – 40’ high
  set a minimum of 6’ below grade on the low side of the sloped grade
    Publication 408 Sections 910.3(k) & 1101.11(a)
Manual Section 6.2

## Slide 23: Electrical Service Type A (Wood Poles)
  Verify that poles are tall enough to provide proper vertical clearances for all attached wires, span wires and cable

## Slide 24: Electrical Service Type A (Wood Poles)
  Verify that a minimum, 2” diameter, hot-dipped galvanized rigid metallic conduit with a service head is used

## Slide 25: Electrical Service Type A (Wood Poles)
  Verify that conduit straps are no further apart than 4’ center to center

## Slide 26: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)

## Slide 27: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify that contractor coordinates with the utility company for location of the service feed

## Slide 28: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify that a minimum, 2” diameter, hot-dipped galvanized rigid metallic conduit with service head is used for service
  unless otherwise required by the utility company
    TC-8804 Sheet 1, Publication 408 Section 954 & 1101.09

## Slide 29: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify that conduit straps are no further apart than 4’ center to center. TC-8804 Sheet 1
  Verify the contractor coordinates the meter type and socket with the utility company. Publication 408 Section 1104.05(d)3

## Slide 30: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify that a service disconnect without an external handle is included
    TC 8804 Sheet 1, Publication 408 Sections 954 & 1104.05(d)

## Slide 31: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify there is a 1” minimum diameter conduit in pole foundation with #4 AWG minimum grounding conductor to ground rod in earth adjacent to pole foundation
  Verify the minimum clearance as indicated in Pub 149 is obtained
    TC- 8801 sheet 1

## Slide 32: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify the electrical utility inspection occurred or was waived by the utility company
    Publication 408, Section 954.3 (f))

## Slide 33: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Verify that non-shrink mortar is used beneath the base plate in paved areas and metal screening is placed beneath the base plate in unpaved areas
    Pub. 408 sec. 951.3(c) TC- 8801

## Slide 34: Electrical Service Type B (Steel Poles)
Electrical Service Type B (Steel Poles)
  Clearances vary by facility, voltage and owner
    If there is a question of appropriate clearance, contact the District Utility Administrator

## Slide 35: Electrical Service, Type C
Electrical Service, Type C (Installed on base mounted controller cabinet)

## Slide 36: Electrical Service, Type C
Electrical Service, Type C (Installed on base mounted controller cabinet)
  Verify the contractor coordinates the meter type and socket with the utility company
    Publication 408 Section 1104.05 (d)3)
  Verify that a minimum 2” diameter hot dipped galvanized rigid metallic conduit and fittings are used for service unless otherwise required by the Utility
    TC-8804

## Slide 37: Electrical Service, Type C
Electrical Service, Type C (Installed on base mounted controller cabinet)
  Verify that a galvanized rigid steel 2” conduit is used between the meter and the disconnect enclosure
    TC-8804
  Verify that a galvanized rigid steel 2” conduit and fittings are used between the disconnect enclosure and the controller cabinet
    TC-8804

## Slide 38: Meter Socket and Disconnect (All Service Types)
Meter Socket and Disconnect (All Service Types)
  Verify the contractor coordinates the meter type and socket with the utility company
    Publication 408 Section 1104.05 (d)3)

## Slide 39: Meter Socket and Disconnect (All Service Types)
  Verify that a minimum 2” diameter hot dipped galvanized rigid metallic conduit and fittings are used for service unless otherwise required by the Utility
    TC-8804
  Verify that a galvanized rigid steel 2” conduit is used between the meter and the disconnect enclosure
    TC-8804

## Slide 40: Meter Socket and Disconnect (All Service Types)
  Verify that a galvanized rigid steel 2” conduit and fittings are used between the disconnect enclosure and the controller cabinet
    TC-8804
  Verify that ungrounded conductors, grounded conductors, and equipment grounding conductors to traffic controller are a minimum of #8 AWG.
    TC-8804

## Slide 41: Meter Socket and Disconnect (All Service Types)
  Verify that a galvanized steel, stainless steel, or aluminum service enclosure with hinged door and provisions for a padlock conforming to NEMA Standard Type 3R, 3S, or 4 is provided
    Publication 408 Section 1104.05(d)4.a

## Slide 42: Meter Socket and Disconnect (All Service Types)
  Verify the ground wire is either bare or green insulated #8 AWG minimum
    Publication 408 Section 1104.05(b)3
  Verify the grounding electrode from service is connected to the grounding lug inside the enclosure with a #4 AWG conductor
    Publication 408 Section 1104.05(f) & TC-8804

## Slide 43: Traffic Signal Structural Supports
Refer to Publication 408 Sections 951 and 1104.02 for further details
Manual Section 6.3

## Slide 44: Foundations
Foundations
  Field-verify that traffic signal supports are located in accordance with the approved plans and the minimum clearance as indicated in Pub 149 is obtained
    TC-8801 sheet 1

## Slide 45: Foundations
Foundations
  Verify the "Pennsylvania One Call System (#811)" notification was completed by the contractor and all acceptable clearances were obtained
  Contact the District Signal Supervisor to resolve any conflicts between existing utilities and the plan location of any support foundation

## Slide 46: Foundations
Foundations
  Verify the elevations for the traffic signal support foundations ensure proper clearance above the roadway to the bottom of signal heads and/or signs and/or tether wire
    The signal contractor is responsible for coordination with the prime contractor in determining pole foundation elevations
    Changes to grades shown on the drawings must be factored into the signal contractor's determination of shaft height and foundation elevations
    See TC 8801

## Slide 47: Foundations
Foundations
  Verify foundation type, depth and rebar configuration in TC- 8801, which are determined by the following:
    Approved Traffic Signal Support-mast arm length
    Approved Traffic Signal Support-Strain Pole-design tension and shaft length
  For a foundation within a sidewalk area, verify the top of the foundation will be flush with the final finished surface

## Slide 48: Foundations
Foundations
  For a foundation outside a paved sidewalk, verify the top of the foundation will be at least 6“above the surrounding surface
  Verify that anchor bolts are clean, protected and placed at the same elevation. Verify the bolt projection is sufficient to rake the support properly

## Slide 49: Foundations
Foundations
  Verify the contractor has used the proper length anchor bolt considering the required embedment length and required projection as shown on TC-8801
  Verify that all conduits are in place and will be able to fit within the footprint of the pole when it is set. The conduits must have 24” of cover to the top of subbase when they exit the foundation

## Slide 50: Traffic Signal Supports
Traffic Signal Supports
  Verify that traffic signal supports were inspected in the fabrication plant in accordance with Publication 408 Section 1104.01

## Slide 51: Traffic Signal Supports
Traffic Signal Supports
  Verify that base plate anchor bolts, nuts and washers are installed and tightened in accordance with Publication 408 Section 1104
    Verify the distance between the bottom of each leveling nut and the concrete foundation is less than the bolt diameter

## Slide 52: Traffic Signal Supports
Traffic Signal Supports
  Verify the center line of the hand hole is 18” above the base plate
    TC-8801
  Verify the minimum area of hand hole is 25 square inches with a minimum unobstructed width of 3.5”
    TC-8801

## Slide 53: Traffic Signal Supports
Traffic Signal Supports
  Verify the opening in the hand hole frame is 7” in height, 3 1/2” in width, cut from 3” thick plate and protrudes from pole ¾” minimum
    TC-8801 sheet 10

## Slide 54: Traffic Signal Supports
Traffic Signal Supports
  Verify the cover plate is ¼” x 5” x 8” with a neoprene gasket cemented on and that it is tightly secured to the pole with fasteners
    TC-8801
  Verify the ground lug is attached to the hand hole frame within the pole cavity
    TC-8801

## Slide 55: Mast Arms
Mast Arms
  Verify the hand hole is installed 90o or 180o from the centerline of arm “A.”
    TC-8801
  Verify that approved and tested high-strength bolts, nuts and washers are used to connect the mast arm to the pole shaft

## Slide 56: Mast Arms
Mast Arms
  Verify the observations for galloping as required by TC- 8801, sheet 1 of 10, note 16 are made
  Clearances vary by facility, voltage and owner. If there is a question of appropriate clearance, contact the District Utility Administrator

## Slide 57: Strain Pole
Strain Pole
  Verify, with a visual inspection from the ground, that the span wire is attached using a clamp with dead-end, feed-thru, strand-vise with stainless steel bail
    TC-8801

## Slide 58: Strain Pole
Strain Pole
  Verify, with a visual inspection from the ground, that the bonding clamp is suitable for use with any combination of copper, steel, or aluminum conductors
    TC-8801

## Slide 59: Strain Pole
Strain Pole
  Verify, with a visual inspection from the ground, that the span wire and the tether wire are electrically bonded to the strain pole
  Use a minimum #4 AWG bare copper, connected to the span wire and tether wire and attached with a lug to the strain pole or another method that assures electrical connectivity
    TC-8801

## Slide 60: Strain Pole
Strain Pole
  Clearances vary by facility, voltage and owner
  If there is a question of appropriate clearance, contact the District Utility Administrator.

## Slide 61: Strain Pole
Strain Pole
  Verify that all tether clamps used to secure the bottom of a sign or signal head to a tether wire have sheet lead wrapped over the tether wire at the clamp connection and the lead extends out both sides of the clamp approximately 1/4”.
  Verify the tether cable clamp at the bottom of the signal housing is positioned correctly per TC-8801, Detail III.

## Slide 62: Strain Pole
Strain Pole
  Verify the span wire used has breaking strength equal to or exceeding the design tension
    TC-8801

## Slide 63: Strain Pole
Strain Pole
  Verify that signal heads are attached with span wire hanger, balance adjuster, cable entrance adapter and pipe as required to place top of all signs and signal heads at the same elevation
    TC-8801

## Slide 64: Strain Pole
Strain Pole
  Verify that ¼” diameter tether wire is used
    TC-8801

## Slide 65: Strain Pole
Strain Pole
  Verify that lashing of the distribution cable to the span wire is accomplished with one of the following:
    Preformed galvanized steel rods
    Self-locking cable ties of outdoor type
    Solid copper wire
    Galvanized steel wire
    Stainless steel wire
    Cable rings and saddles

## Slide 66: Strain Pole
Strain Pole
  Verify that wire lashing makes one complete wrap at intervals not exceeding 6”
  Verify that ends of wire lashing are secured to the span wire with an all-purpose split bolt connector
  Verify that cable ties are at intervals not exceeding every 12”

## Slide 67: Strain Pole
Strain Pole
  Verify the cable entrance is a minimum of 4” in diameter
    TC-8801
  Verify, with a visual inspection from the ground, that an insulated grommet is used for weather proofing the wire inlet.
    Publication 408 Section 1104.02(a)6

## Slide 68: Strain Pole
Strain Pole
  Verify, with a visual inspection from the ground, the span wire and an individual clamp is used for each span wire or tether wire
    TC-8801

## Slide 69: Strain Pole

## Slide 70: Pedestal Poles
Pedestal Poles
  Verify the pole is tall enough to provide 8’ minimum, 10’ maximum height above grade to bottom of signal housing
    TC -8803

## Slide 71: Pedestal Poles
Pedestal Poles
  Verify that hand hole opening is 3” x 5” with a minimum frame thickness of 3/8” and the centerline is 18” above the base plate
    TC-8803 and TC-8801
  Verify the base plate is continuously welded to the pole
    TC-8803

## Slide 72: Pedestal Poles
Pedestal Poles
  Verify that non-shrink mortar is used beneath the base plate in paved areas and metal screening is placed beneath the base plate of the pole in unpaved areas
    Pub. 408 sec. 951.3 (c))
  After erection of pole and mounting of signal hardware, verify the minimum clearance as indicated in Pub 149 is obtained from curb to the nearest element of the pole or signal head
    TC-8801, TC-8803

## Slide 73: Pedestrian Pushbutton Poles
Pedestrian Pushbutton Poles
  Verify that poles are placed correctly in relation to the location of the curb ramps
    TC-8803
  Verify the pole foundations are correct for the type of pushbutton pole being installed TC-8803

## Slide 74: Pedestrian Pushbutton Poles
Pedestrian Pushbutton Poles
  Verify the poles are 3” Galvanized Rigid Steel Conduit, except Type C and Type F poles which should be 4.5” O.D. Schedule 40
    TC-8803
  Verify the top of the pole is 60” (5’) above finished grade and that a galvanized steel or aluminum cap is in place
    TC-8803

## Slide 75: Pedestrian Pushbutton Poles
Pedestrian Pushbutton Poles
  Verify that all accessibility features are compliant with PennDOT Publication 13M (DM-2), Chapter 6, Publication 72M (RC Standards) criteria and Publication 149
    TC-8803

## Slide 76: Pedestrian Pushbutton Poles
Pedestrian Pushbutton Poles
  Verify the top of the foundation is flush with the surface of adjacent pavement when installed in pavement and that there is a 1/2" pre-molded expansion joint filler between foundation and adjacent pavement
    TC-8803

## Slide 77: Pedestrian Pushbutton Poles
Pedestrian Pushbutton Poles
  Verify that if a pedestrian pushbutton extension arm is used, it is 3” or less. If it measures between 3" to 12", obtain District Office approval prior to installation
  Do not allow installation of arms longer than 12”
    TC-8803

## Slide 78: Wood Poles
Wood Poles
  Verify that temporary wood poles are in accordance with Publication 408 Section 1104.02(f).
  Verify the contractor installs service poles in accordance with Publication 408 Section 910.3(k).

## Slide 79: Traffic Signal Subsurface Facilities
Refer to
  Publication 408 Sections 954
  1104.05
Manual Section 6.4

## Slide 80: Trench and Backfill
Trench and Backfill
  Trench and Backfill Type I (in earth)
    Verify the trench is wide enough to allow proper installation, backfill and compaction of the trench and that at least 1” can be maintained between each conduit and between the conduit and the edge of the trench
    Verify the trench is deep enough to provide at least 24” of cover to the top of the conduit
      TC-8806

## Slide 81: Trench and Backfill
Trench and Backfill
  Trench and Backfill Type I (in earth)
    Verify that plastic marking tape is placed in the last layer of back-fill material for the entire length of the trench
      Publication 408 Section 910.3.(c)

## Slide 82: Trench and Backfill
Trench and Backfill (sidewalk or paved shoulder)
    Verify that special provisions do not call for special actions including full sidewalk slab replacement
    Verify the sidewalk or paved surface is saw-cut at the nearest construction joint

## Slide 83: Trench and Backfill
Trench and Backfill
  Verify the trench is wide enough to allow proper installation, backfill and compaction of the trench and that at least 1” can be maintained between each conduit and between the conduit and the edge of the trench
  Verify that plastic marking tape is placed in the last layer of back-fill material for the entire length of the trench
    Publication 408 Section 910.3.(c)

## Slide 84: Trench and Backfill
Trench and Backfill
  Verify that plastic marking tape is placed in the last layer of back-fill material for the entire length of the trench
    Publication 408 Section 910.3.(c)
  Verify the sub-base is replaced in kind
  Verify the pavement surface is replaced in kind

## Slide 85: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type III)
    Verify the trench is wide enough to allow proper installation, backfill and compaction of the trench and that at least 1” can be maintained between each conduit and between the conduit and the edge of the trench
    Verify the surface on each side of the trench is saw-cut to a minimum depth of 3”
    Verify the trench is deep enough to provide at least 24” of cover from the top of the conduit to the bottom of the sub-base

## Slide 86: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type III)
    Verify that bedding soil for the conduits has been placed at the bottom of the trench
      Publication 408 Section 206.2(a)
    Verify the contractor backfills the trench as soon as possible
    Verify that plastic marking tape is placed in the last layer of backfill material for the entire length of the trench
      Publication 408 Section 910.3.(c)

## Slide 87: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type III)
    Verify the sub-base is replaced as specified within the construction plans or as specified in Publication 408 Section 954
    Verify the trench is backfilled with Class A cement concrete up to the bottom of the existing sub-base
    Verify the pavement is restored as specified in Publication 408 Section 954

## Slide 88: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type IV)
  TC-8804 Sheet 2 and Publication 408 Section 954.3
  Verify the trench is wide enough to allow proper installation, backfill and compaction of the trench and that at least 1” can be maintained between each conduit and between the conduit and the edge of the trench

## Slide 89: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type IV)
  TC-8804 Sheet 2 and Publication 408 Section 954.3
  Verify the surface on each side of the trench is saw-cut to a minimum depth of 3”
  Verify the trench is deep enough to provide at least 24” of cover from the top of the conduit to the bottom of the sub-base

## Slide 90: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type IV)
  Verify that bedding soil for the conduits has been placed at the bottom of the trench
    Publication 408 Section 206.2(a)

## Slide 91: Trench and Backfill
Trench and Backfill
  Trench in Roadway (Type IV)
  Within the last layer of backfill for the entire length of the trench
    Publication 408 Section 910.3.
  Verify the sub-base and pavement are both replaced as specified within the construction plans or as specified in Publication 408 Section 954

## Slide 92: Directional Boring
Directional Boring
  Publication 408 Section 954.3(b)
  Verify the contractor has the appropriate erosion and sedimentation control measures in place prior to boring
  Verify that boring pits are a minimum of 2’ from the edge of roadway

## Slide 93: Directional Boring
Directional Boring
  Publication 408 Section 954.3(b)
  Verify that boring is below the existing roadway sub-base layer
  Verify that boring pits are covered with adequate protection if the drilling operation is left overnight
  Do not allow the use of pneumatic hammers

## Slide 94: Conduit
Conduit

## Slide 95: Conduit
Conduit
  Verify that all PVC conduit, conduit fittings, and conduit elbows are all supplied from the same manufacturer
  Verify the cement is labeled by or recommended by the conduit manufacturer
  Verify that expansion/ deflection fittings are provided for conduit mounted on or within structures. Standard Drawing BC 721M (BC -721)

## Slide 96: Conduit
Conduit
  Verify that conduit ends within junction boxes or foundations are restricted with a rodent-proof filler
    Publication 408 Section 954.3(c)
  Verify the conduit maintains at least 12” separation from other underground utilities
    Publication 408 Section 954.3(c)
  Verify that high-impact spacers are in place every 8’ on center if more than two rigid non-metallic conduits are installed in a common trench
    Publication 408 Section 954.3(c)

## Slide 97: Conduit
Conduit
  Verify that underground conduits are at least 2” diameter unless otherwise specified. Publication 408 Section 910.3(g) & TC- 8804 Sheet 1
  Verify that each conduit has a bell end or bushing to protect cables leaving the conduit

## Slide 98: Junction Boxes
Junction Boxes

## Slide 99: Junction Boxes
Junction Boxes
  Verify dimensions of the junction box based on box type and approved CS 201 Form
  Verify there is a minimum of 2 cubic feet of coarse aggregate (#57 or #8) under all junction boxes
  Verify that Type JB-26 and JB-27 are not located in a vehicular traffic area

## Slide 100: Junction Boxes
Junction Boxes
  Verify the rim of the box is 1” above final grade in earth or flush with final grade in paved surface areas
  Verify the lid is non-slip and is secured by a minimum of two corrosion resistant fasteners
  Verify that a water-tight connection to the housing is provided
    Publication 408 Section 1104.05(c)

## Slide 101: Junction Boxes
Junction Boxes
  Verify the words “TRAFFIC SIGNAL” are imprinted on the lid. Publication 408 Section 1104.05(c)
  Verify that cast iron or steel boxes have lids that are hot-dipped galvanized with a closed cell neoprene gasket. Verify that there is a factory-installed grounding stud and hex nut in rear of the box
    Publication 408 Section 1101.10(a) & BC-721M

## Slide 102: Junction Boxes
Junction Boxes
  Verify that ground lugs are used to ground metal parts and that ground wires are not directly connected with the lid
    RC- 81M & RC-82M

## Slide 103: Junction Boxes
Junction Boxes
  Verify the internal depth is in conformance with the depth specified for that type
    TC-8804 Sheet 2
  Verify that if the bottom is closed a 2” minimum drain hole is provided

## Slide 104: Controllers
Refer to Publication 408 Sections 952 and 1104.03 for further details.
Manual Section 6.5

## Slide 105: Approval Listings
Approval Listings
  Verify the controller assembly is on the approved CS-201 Form
  Obtain documentation from the contractor verifying the controller assembly was shop (bench) tested

## Slide 106: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)

## Slide 107: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the plans call for a base mounted (Type I mounting) controller assembly
  Verify the intersection and controller can be observed simultaneously from the proposed location prior to pouring the foundation
  Verify the foundation is 4” larger than the cabinet on all sides

## Slide 108: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the depth of the foundation is 31” plus the diameter of the largest conduit that runs through the foundation
  Verify the concrete pad in front of the controller extends 28” from the cabinet face with a depth tapering from 12” at the cabinet foundation to 6” at the front edge of the concrete pad
  Verify that there is a ¾” chamfer on all sides of the control cabinet foundation

## Slide 109: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the top of the control cabinet foundation is elevated 4” above the finish grade at its lowest point
  Verify that there will be no conflicts between conduits and the cabinet before constructing the foundation
  Verify that a 1” diameter screened drain pipe is installed from the bottom rear of the cabinet to the edge of the foundation, discharging above grade

## Slide 110: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the cabinet anchor bolts cast into the foundation are ½” x 12”
  If anchor bolts are not used, verify that ½” x 3 ¾” expansion bolts are used
  Verify that caulking compound was applied around the entire cabinet enclosure between the base of the cabinet and the concrete foundation
    Verify that caulking is in accordance with Publication 408 Section 705.8

## Slide 111: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the plans call for a base-mounted controller assembly (Type I mounting)
  Verify the intersection and controller can be observed simultaneously from the proposed location and there is no undesirable door opening, such as opening into traffic, prior to pouring the foundation
  Verify the foundation is 4” larger than the cabinet on all sides

## Slide 112: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the depth of the foundation is 31” plus the diameter of the largest conduit that runs through the foundation
  Verify that there is a ¾” chamfer on all sides of the control cabinet foundation
  Verify the top of the control cabinet foundation is elevated 4” above the finish grade at its lowest point

## Slide 113: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify that there will be no conflicts between the conduits and the cabinet before constructing the foundation
  Verify that conduits entering the cabinet are plugged with an approved duct seal formed around the wires to prevent entry from water, insects, snakes or rodents
  Verify that a 1” diameter screened drain pipe is installed from the bottom rear of the cabinet to the edge of the foundation, discharging above grade

## Slide 114: Controller Foundations (TC-8802)
Controller Foundations (TC-8802)
  Verify the cabinet anchor bolts cast into the foundation are ½” x 12”
  If anchor bolts are not used, verify that ½” x 3¾” expansion bolts are used
  Verify that caulking compound was applied around the entire cabinet enclosure between the base of the cabinet and the concrete foundation. Verify that caulking is in accordance with Publication 408 Section 705.8
  Verify that ½” pre-molded expansion joint filler was installed between the foundation and the surrounding paved area

## Slide 115: Controller Cabinets
Controller Cabinets
  Type I Mounting (Ground Mounted)
    Verify the plans call for a base-mounted controller assembly (Type I mounting)
    Verify the controller cabinet is equipped with the following items:
      Full height continuously welded piano hinge. Type 170 - Publication 408 Section 1104.03 (b).2.f NEMA – Publication 408 Section 1104.03 (b)1.f.1

## Slide 116: Controller Cabinets
Controller Cabinets
  Type I Mounting (Ground Mounted)
      Key operated spring lock. Type 170 - Publication 408 Section 1104.03(b)2.f
      Cover vents with full perimeter frame disposable filter securely held in place. NEMA – Publication 408 Section 1104.03(b)1.f.2
      Three-point draw roller type door latching mechanism required. Type 170 - : Publication 408 Section 1104.03(b)2.f NEMA – : Publication 408 Section 1104.03(b)1.f.1
      15” minimum clearance between bottom of cabinet and the terminals, equipment, or devices. TC-8802

## Slide 117: Controller Cabinets
Controller Cabinets
  Verify that conduits entering the cabinet are plugged with an approved duct seal formed around the wires to prevent entry from water, insects, snakes or rodents

## Slide 118: Controller Cabinets
Controller Cabinets
  Type II Mounting (Pole Mounted)
    Verify the plans call for a pole mounted controller assembly (Type II mounting)
    Verify that there is no undesirable door opening, such as opening into traffic
    Verify the bottom of the cabinet is not higher than 27” when the cabinet extends over a sidewalk or walkway

## Slide 119: Controller Cabinets
Controller Cabinets
  Type II Mounting (Pole Mounted)
    Verify the centerline of the cabinet is between 4’-3” and 4’-6” above final grade
    Verify that no portion of any equipment (except fan and light) is higher in the cabinet than the top of the door
      TC-8802
    Verify the door latching mechanism is a three-point draw roller type
      Publication 408 Section 1104.03(b)

## Slide 120: Controller Cabinets
Controller Cabinets
  Type II Mounting (Pole Mounted)
    Verify that vents are covered with a full perimeter, framed, disposable, filter securely held in place
      Publication 408 Section 1104.03(b).1.f.2
    Verify that all terminals, equipment and devices are at least 3” above the bottom of cabinet
      TC-8802

## Slide 121: Manual Test Control
Manual Test Control
  Review the requirements in Publication 408 for the type of controller:
    Type 170
      Sections 1104.03 (b)2.b & 1104.03(b)2.f
    NEMA
      Section 1104.03(b)1.b
    Type 2070
      Section 1104.03(b)3.b

## Slide 122: Manual Test Control
Manual Test Control
  Verify the manual control panel includes a method to switch the signal from automatic to manual control
  Verify the manual control panel is in a watertight enclosure compartment accessed separately from the main control cabinet and locked with a standard police key
  Verify the plug-in hand control cable is neatly tucked in the enclosure

## Slide 123: Grounding Assemblies
Grounding Assemblies
  Verify that ground rods are copper clad steel, at least 5/8” diameter and at least 10’ long
    TC-8804
  Verify that ground rods are connected to the grounding bus in the service disconnect and/or support with a #4 AWG (min) bare copper ground wire
    TC-8804

## Slide 124: Grounding Assemblies
Grounding Assemblies
  Verify the ground wire is connected to the ground rod with either a bronze connector or an exothermic weld and the connection is coated with approved corrosion inhibitor
    Publication 408 Section 1101.11(j) & TC-8802 & TC-8804
  Note the ground rod is to be installed outside the foundation of the cabinet or support
    TC-8804
  Test in accordance with 910.3(q)

## Slide 125: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify the wiring and installation is done in a neat and workmanlike manner with all cables tie-wrapped
    Publication 408 Section 952.3(d)1
  Verify the spare conductors of signal cable and interconnection cable are neatly wrapped in the cabinet and are the same length as the active conductors
    Publication 408 Section 952.3(d)1

## Slide 126: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify the conduit entry stubs are at least 3” high
    TC- 8802
  Verify there is a minimum of 15” between the bottom of the cabinet and terminals, equipment, and devices
    TC-8802

## Slide 127: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify that a #8 AWG equipment grounding conductor is connected to the service disconnect
    TC-8804
  Verify there is only one conductor per screw on the terminal block or use pressure-type mechanical lugs for multiple conductors
    Publication 408 Sect. 954.3(e)1

## Slide 128: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify the wiring and cables are neatly arranged and tiewrapped
    Publication 408 Section 952.3(d)1
  Verify that RFI Line Filter conforms to Publication 408 Section 1104.03 (c)3.b.
  Verify the chassis ground bar is connected to the grounding system.
  Verify the surge protection conforms to Publication 408 Section 1104.03(c)3.c.

## Slide 129: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify that equipment is positioned in the cabinet so that all terminal strips are accessible without removing other equipment
    Publication 408 Section 1104.03(b)2.f
  Verify the wiring and installation is neat with all cables tie-wrapped
    Publication 408 Section 952.3(d)1

## Slide 130: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify that all grounding conductors have green insulation or are wrapped all the way around in green marking
  Verify that all neutral conductors have white insulation or are wrapped all the way around in white marking
  Verify that all wires are labeled with a unique wire or terminal number that indicates where it is to be connected

## Slide 131: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  If specified, verify that access to the transfer switch and twist lock receptacle for connection to an emergency generator is installed behind a locked enclosure with police access
    Publication 408 Section 1104.03(b)2.f
  Verify there is a transfer switch relay to disconnect the permanent power source and connect the emergency power source
    Publication 408 Section 1104.03(b)2.f

## Slide 132: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify there is a Ground Fault Circuit Interrupter (GFCI) protected convenience outlet on a dedicated 20 amp minimum circuit
    Publication 408 Section 1104.03(b)2.f

## Slide 133: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  If specified, verify there is a UPS/Battery back-up capable of a minimum four-hour back-up operation
    Publication 408 Section 1104.05(i)
  If specified, verify that a fiber optic patch panel is included
  If specified, verify that a fiber optic cable loop is included

## Slide 134: Control Equipment and Wiring Installation
Control Equipment and Wiring Installation
  Verify that all equipment indicator lights are not blocked and can be seen from the cabinet doorway. Publication 408 Section 1104.03(b)2.f
  Verify that all equipment is installed upright and on its own rack or shelf and not stacked on top of other equipment. Publication 408 Section 1104.03(b)2.f
  Verify there is adequate room within the cabinet for equipment and servicing. Publication 408 Section 1104.03(b)2.f

## Slide 135: Programming and Timing
Programming and Timing
  Verify with the District Signal Supervisor the timing plans and operation shown on the plan is correct and to be used at time of “turn on.”
  Verify the correct timing plans and operation shown have been programmed into the controller properly. Call the District Signal Supervisor, if required, to confirm correct programming
  With the contractor, observe controller operation with the traffic signals “off” to verify correct controller programming

## Slide 136: Signal Indications
Refer to Publication 408 Sections 955 and 1104.06 for further details.
Manual Section 6.6

## Slide 137: Vehicular
Vehicular
  Verify the signal housing and LED modules are the size and color specified on the traffic signal plan. Highway yellow is the standard signal housing color unless otherwise noted. Publication 408 Section 1106(a)1
  Verify that overhead signals are installed with the top of the signal head at the same elevation prior to installing the tether wire. TC-8801 Sheet 2

## Slide 138: Vehicular
Vehicular
  Verify that drip loops at wire entrances to signal heads are secured with acceptable outdoor type cable ties. Publication 408 Section 954.3(e)1 & 1104.05(b)5
  Verify there is a grommet at the wire entrance to the mounting bracket. TC-8801 Sheet 1

## Slide 139: Vehicular
Vehicular
  If optically programmed signal heads are specified, verify the contractor coordinates the field programming of the signal heads with the District Signal Supervisor for cut-off and distance limiting.
  Verify the specific locations of overhead vehicular signal heads are as shown on the traffic signal permit plan.
  Verify the vehicular signal heads are generally aimed at approaching traffic that is 150’ in front of the stop line.

## Slide 140: Vehicular
Vehicular
  Verify mounting hardware which includes:
    Span wire hanger (span wire installations)
    Balance adjuster
    Cable entrance fitting (mast arm installations)
    Pipe, as required, to keep the tops of all signal heads at the same elevation.

## Slide 141: Vehicular
Vehicular
  Verify that cable entrance fitting is positioned so the cable entrance will be from the backside of the signal housing.
  Verify the visors, louvers and back plates indicated on the plan or in the specifications have been installed properly.
  Verify there is 15’ to 19’ of vertical clearance for overhead signal housings, unless otherwise specified on the traffic signal permit plan.
  Verify the minimum clearance as indicated in Publication 149 is obtained from curb or edge of shoulder to the post-mounted signal housings. TC-8801

## Slide 142: Pedestrian
Pedestrian
  Verify the type of pedestrian signal head housing and LED Modual (Type A or Type B) is as called for on the plan.
  Verify the signal housing is the color specified on the plan or in the specifications. Highway yellow is the standard color unless otherwise noted. Publication 408 Section 1106(a)1

## Slide 143: Pedestrian
Pedestrian
  Verify the signal housing is constructed of aluminum or polycarbonate resin. The contractor has the option to provide either unless otherwise specified. Publication 408 Section 1106(a)1
  Verify the minimum clearance as indicated in Publication 149 is obtained from curb or edge of shoulder to the post-mounted signal housing. TC-8801

## Slide 144: Pedestrian
Pedestrian
  Verify the bottom of the signal head is between 7’ and 10’ above the sidewalk. If there is no sidewalk, verify the bottom of the signal head is between 7’ and 10’ above the pavement grade at the centerline of the road. TC-8801

## Slide 145: Preemption Fail Safe Indications
Preemption Fail Safe Indications
  Verify that emergency vehicle preemption is specified and shown in the movement phase diagram.
  Verify the size and color of the confirmation light supplied by the contractor is in accordance with the specifications. Coordinate with the District Signal Supervisor and the municipality.
  At signals with emergency vehicle preemption on intersecting approaches, verify that confirmation lights are associated with the proper approach.
  Verify that pre-empt receivers are mounted in the right location and pointed in the correct direction.

## Slide 146: Electrical Distribution
Refer to Publication 408 Sections 954 and 1104.05 for further details.
Manual Section 6.7

## Slide 147: Grounding
Grounding
Publication 408 Section 954.3(d) and Section 1104.03(d)
  Verify that a continuous mechanical and electrical grounding system exists connecting the following items:
    Service disconnect enclosure
    Controller assembly and cabinet
    Traffic signal supports
    Ground rods
    Span wires
    Tether wires
    Steel conduit
    Metallic junction boxes
  Verify that Underwriter’s Laboratory listed bonding/grounding bushings are installed on the ends of all steel conduits and the bushings are connected to the grounding system.

## Slide 148: Signal Cable, Wiring and ID Tags
Signal Cable, Wiring and ID Tags
  Verify that all signal cable, wiring and ancillary equipment are included on the CS-201 Form.
  Verify that lubricant is used to install cable in the conduit. If new cable is installed in existing conduit, verify the conduit was cleaned in accordance with Publication 408 Section 910.3.

## Slide 149: Signal Cable, Wiring and ID Tags
Signal Cable, Wiring and ID Tags
  Verify that signal wires and cables are spliced only in pole bases using waterproof resin-filled wire nuts.
  Verify that ground wires are spliced only in junction boxes.
  Verify that all cables at splices in pole bases or cabinets are properly labeled or have ID tags attached.
  Verify that all terminal connections have been banded and the appropriate coding used in accordance with Publication 408 Section 954.3.

## Slide 150: Signal Cable, Wiring and ID Tags
Signal Cable, Wiring and ID Tags
  Verify that all spare and unused conductors have been terminated on the ground buss.
  Verify that enough signal cable slack is left for proper wiring connections and drip loops.
  For span wire installations, verify the cable is lashed to the span wire in accordance with TC-8801.
  Verify that drip loops have been included in all signal cables entering signal head housings. Verify the cable enters the signal head housing at an upward angle to prevent water from entering the signal head. Verify the drip loops are secured with outdoor-type, self-locking cable ties. TC-8801

## Slide 151: Wiring Diagrams
Wiring Diagrams
  Publication 408 Section 1104.01(d)
  Verify the contractor provides three copies of the cabinet wiring diagram and manufacturer's timing plan for each controller assembly
    If there are changes to the timing plan during testing, three new sets of timing plans are required

## Slide 152: Testing
Testing
  1. Verify the contractor certifies all equipment and material has been checked and is in operating order prior to it being energized
  2. Verify and document the faulty or defective material that was removed and replaced to correct the condition that halted the test
  3. Test grounding system in accordance with Publication 408 Section 910.3 (q)

## Slide 153: Detection
Refer to Publication 408 Sections 956 and 1104.07 for further details.
Manual Section 6.8

## Slide 154: Vehicular
Vehicular
  Inspector In-Charge determines in which paving layer (wearing course, base course or “pre-formed” under new concrete pavement) the plans or specifications call for the loop sensor to be installed
  Verify that sensors are located as indicated on the plan. Verify the saw-cutting will not go through pavement joints or areas of deteriorating pavement. Contact the District Signal Supervisor if there are any questions prior to installing loops.

## Slide 155: Vehicular
Vehicular
  Verify the loop layout is in accordance with TC-8806 and the saw cut depth is constant for the entire loop sensor.
  Verify the slot is cleaned of moisture and debris, preferably with a compressed air hose.
  Verify the loop sensor wire is #14 AWG, IMSA Specification 51-5. It is an insulated wire inside a PVC tube. Publication 408 Section 1104.07(b)1.a.
  Verify that each saw cut slot has the required number of turns of sensor wire per detector as required to provide the specified inductance.

## Slide 156: Vehicular
Vehicular
  Verify that all wires in a common slot are proceeding in the same direction.
  Verify the sensor wire is tamped into the slot with a nonmetallic tool.
  Verify the saw cut ends one foot (1') from the edge of pavement and a rotary drill is used to make a hole in the pavement. Verify the sensor wire is installed through conduit to the junction box by trenching through either the shoulder or sidewalk.
  Verify the splice of the sensor wire to the lead-in wire is made only inside the junction box. Verify there is no other splicing of sensor wire. TC-8806.

## Slide 157: Vehicular
Vehicular
  Verify the ends of the conduit are properly sealed with duct seal after the sensor wire is installed. TC-8806.
  Verify the amplifiers are on the approved CS-201 Form.
  Verify the values of the tests of the sensor after installation for leakage resistance, series resistance, and inductance before sealing the saw cut slot. Publication 408 Section 956.03(a)1 Cutting, Placing Wire and Sealing

## Slide 158: Vehicular
Vehicular
  Verify the sealant used to seal the saw cut is in Bulletin 15 and the manufacturer’s specifications for mixing and installation are followed. Verify the sealant is not placed when the temperature is under 32° F or during precipitation. Publication 408 Section 956.03(a)1
  Verify the slot is filled to within 1/8" of the pavement surface
  Verify the excess sealant is removed, but not with the use of solvents. Do not allow traffic on the sealant until it is properly cured

## Slide 159: Vehicular
Vehicular
  Verify that location of the sensor wire is marked after installation to ensure that core samples do not sever the wire
    Verify that all excess loop sensor wire or lead-in wire is banded in the junction box to prevent movement which will result in false calls
    Verify after testing inductance, a copy of the inductance readings is placed, along with the make and model number of the testing equipment, in the controller cabinet

## Slide 160: Vehicular
Lead-in Cable and Splicing
  Verify that detector lead-in cable is #14 AWG, IMSA Specification 50-2
    Publication 408 Section 1104.07(a)2
  Verify the detector lead-in cable is installed in one continuous length to the terminal strip in the controller cabinet
    No splices are allowed in the lead-in cable.
  Verify the detector lead-in cable is spliced to the sensor wires as shown in TC-8806 or by using another approved method.

## Slide 161: Vehicular
Amplifiers
Verify that after connecting to the loop amplifier, the amplifier has been adjusted as per the manufacturer’s instructions to obtain the necessary sensitivity
  Verify that no “false” calls are being placed by traffic moving in the opposite direction
Verify the loop amplifiers are labeled with the correct phase and movement

## Slide 162: Vehicular
Vehicular
  Video Detection
  Verify the video detection camera is mounted at the highest point possible.
  Verify that each camera is provided with a sun shield.

## Slide 163: Vehicular
Vehicular
  Video Detection
  Verify that all cables and connections are per the manufacturer’s specifications
  Verify that each zone of video detection on the plans is covered by the system

## Slide 164: Pedestrian Pushbuttons
Pedestrian Pushbuttons
  Standard Pushbutton
  Verify the pedestrian pushbutton is installed so the centerline of the pushbutton is between 40” to 44” above the top of the foundation.
  Verify the pedestrian pushbuttons are at least 2” in diameter.

## Slide 165: Pedestrian Pushbuttons
Verify that pushbuttons are located as per the plan. Coordinate with the District Signal Supervisor regarding any changes or questions prior to installation. TC-8803
Verify that vandal-proof (difficult to remove without special tools) stainless steel hardware is used to attach the pushbutton to the support.

## Slide 166: Pedestrian Pushbuttons
Verify the hole in the support was de-burred after drilling but prior to cable installation.
Verify that sealant was placed at the top of the pushbutton where it contacts the support.
Verify by field test that the proper phase and timing is called when the pushbutton is actuated.

## Slide 167: Accessible Pedestrian Signal
Accessible Pedestrian Signal
  Verify the pedestrian pushbuttons are at least 2” in diameter.
  Verify that pushbuttons are located as per the plan. Coordinate with the District Signal Supervisor regarding any changes or questions prior to installation. TC-8803
  Verify that vandal-proof (difficult to remove without special tools) stainless steel hardware was used to attach the pushbutton to the support.

## Slide 168: Accessible Pedestrian Signal
Accessible Pedestrian Signal
  Verify the hole in the support was de-burred after drilling but prior to cable installation.
  Verify that pushbutton, speaker and vibrotactile device are attached to the support with the proper orientation to the applicable crosswalk. Verify that speakers are not attached to pedestrian indications.
  Verify that sealant was placed at the top of the pushbutton, speaker and vibrotactile device where they contact the support.

## Slide 169: Accessible Pedestrian Signal
Accessible Pedestrian Signal
  Coordinate with the District Traffic Signal Supervisor to verify the types of audio messages to be used.
  Verify by field test the proper phase, audio messages and timing are called when actuated.
  Verify the message displayed/operations of accessible pedestrian signals when emergency vehicle preemption is invoked.
  If volume of pedestrian signals does not self-adjust to ambient noise, manual adjustments will be required.

## Slide 170: Preemption Systems
Preemption Systems
  Verify which type of preemption system is required by the plans and specifications
    Audio,
    Optical, or
    Global Positioning Satellite (GPS)

## Slide 171: Preemption Systems
Preemption Systems
  Verify the detector/receiver location prior to installation. A minimum distance of 500’ away from the stop bar on the appropriate approach is recommended for a detection of an actuating vehicle.
  Verify that any training requirements called for in the specifications are followed and that appropriate personnel are trained.

## Slide 172: Preemption Systems
Preemption Systems
  If there are issues with detection, work with vendor to test emergency vehicle sirens/emitters to confirm vehicles meet specifications.
  If possible, it is desirable to test the preemption system with the municipality’s actual responding units.

## Slide 173: Other Preemption Systems
Other Preemption Systems
  Seek guidance from the Distric Traffic Signal Supervisor when railroad preemption or other complex signal operations are indicated.

## Slide 174: Pavement Markings and Signs
Pavement Marking Locations
  Verify the location of crosswalks and stop lines with the District Traffic Signal Supervisor prior to placement.
  Verify coordination of pavement marking and detection zone locations.
Manual Section 6.9

## Slide 175: Placement of Pavement Marking Material
Placement of Pavement Marking Material
  Verify the type of pavement marking material called for in the plan is applied in the field.
  Coordinate the application of the pavement marking material with the contractor to ensure the material is applied at the correct time in the project progress and the weather and pavement conditions are in accordance with the manufacturer’s specifications.

## Slide 176: Sign Types and Locations
Sign Types and Locations
  Verify the type of sign installation and location with the District Signal Supervisor prior to installation
    PUB 111M
  Verify the signs provided are from an approved sign manufacturer and the supplier’s PennDOT identification number is on the back of each sign
  Verify the date of installation is placed on the back of the sign with a permanent marker
  Verify the faces of new signs are covered until project conditions are appropriate for their display

## Slide 177: Traffic Signal Systems
Refer to Publication 408 Sections 953 and 1104.04 for further details.
Equipment
  Verify the location of the master controller, master coordinating unit, or server matches the plans
  Verify the required arrangements have been made with the municipality and the utility that will provide the communications connection
Manual Section 6.10

## Slide 178: Software
Software
  Verify the installation of the proper number of traffic signal system software packages, typically two: one package on a designated municipal computer and the other package on a designated Department computer
    Publication 408 Section 953.3(d)1
  Verify that all project-specific intersection graphics, intersection data, overall system mapping, timing plans and other software programming has been completed
    Publication 408 Section 953.3(d)2

## Slide 179: Training
Training
  Verify the proper amount of training on the traffic signal system software has been completed
    Amount of time varies by project
    Coordinate with the District Signal Supervisor
    Publication 408 Section 953.3(d)3

## Slide 180: Communications
Communications
  Verify the appropriate radio units are installed at the master controller and the local controllers and that each radio unit has repeater capability
  Verify the correct type of antenna is installed at each intersection as per the plan and the antenna is pointed in the correct direction

## Slide 181: Communications
Communications
  Verify that all coaxial cable and antennas are grounded properly and that lightning surge suppressors are installed correctly
  Verify the contractor monitors the radio communication system tests to evaluate and adjust the radio system before use
  Verify the contractor provides all warranties and product information from the contractor for all installed equipment

## Slide 182: Final Inspection and Testing
Inspection, Turn-on Procedures and Flashing Operation (if required)
  After the contractor indicates that a traffic signal installation is ready to be energized and all functional testing (including conflict monitor testing, preemption testing and communication testing) is completed and documented, contact the District Signal Supervisor to schedule a final review and “turn-on”
    Correct any deficiencies found and timing plan changes prior to the “turn on”
    Newly signalized intersections will be put in the “flashing” mode as directed by the District Signal Supervisor
Manual Section 6.11

## Slide 183: Turn-on Procedures and Flashing Operation
Inspection, Turn-on Procedures and Flashing Operation (if required)
  Notify the appropriate municipal personnel to attend the “turn on” and operational testing
    Coordinate with the District Signal Supervisor

## Slide 184: 30-Day Test
30-Day Test
  With the signal in full operation, monitor the 24-hour operating test for not less than 30 consecutive calendar days. Direct the contractor to correct any failure caused by malfunctioning parts or equipment, or faulty workmanship
    The contractor should correct the condition in less than 24 hours after notification -Publication 408, Section 1104.01(g)1
  Energy costs are the responsibility of the contractor during the test period

## Slide 185: 30-Day Test
30-Day Test
  After any failure caused by malfunctioning parts or equipment, or faulty workmanship, is corrected, the 30-day operating test begins anew
    The District Signal Supervisor shall be notified of failure and the restart of the new testing period
    There is no time limit for how long the testing period may last if failures continue to occur
    With the correction of each failure, the 30-day test period begins again
    The signal must operate correctly for 30 consecutive days for the test to be satisfactorily completed

## Slide 186: 180-day Equipment Guarantee Period
180-day Equipment Guarantee Period: (Publication 408 Section 1104.01(g)2)
  After the 30-day test is satisfactorily completed, the 180-day equipment guarantee period begins
    The in-service operation of mechanical and electrical equipment, the controller assembly and related components are included in the 180-day guarantee period
    On HOP projects, it is the responsibility of the municipality to coordinate with the contractor for guarantee issues

## Slide 187: 180-day Equipment Guarantee Period
  During this period the contractor has the following responsibilities:
    Maintain equipment in the controller cabinet. Use additional locks, as necessary, to prevent entry by others.
    Repair faulty workmanship, repair or replace defective materials or equipment, and correct malfunctions in the controller cabinet within 48 hours of commencing repairs.
    Commence repairs no later than the working day following notification of failures or malfunctions.
    Guarantee repairs or replacements for 30 days or the balance of the 180-day guarantee period, whichever is longer.

## Slide 188: Systems Testing
Systems Testing
  Publication 408 Section 953.3(d)1 and Section 953.3(d)2
  Verify that all software packages are in place and functional at the specified municipal location and/or Department computer
  After the successful completion of the 30-day test at every individual intersection, a separate 30-day operations test on the traffic signal system and the related communications system can begin
    This 30-day test is separate and distinct from the 30-day test for each individual intersection

## Slide 189: Systems Testing
  With the signal system in full operation, monitor the 24-hour operating test for not less than 30 consecutive calendar days
    Direct the contractor to correct any failure caused by malfunctioning parts or equipment, software, or faulty workmanship
    The contactor should correct the condition in less than 24 hours after notification

## Slide 190: Systems Testing
  After any failure caused by malfunctioning parts or equipment, software, or faulty workmanship is corrected, the 30-day operating test begins anew
    There is no time limit for how long the testing period may last if failures continue to occur
    With the correction of each failure, the 30-day test period begins again
    The signal system must operate correctly for 30 consecutive days for the test to be satisfactorily completed

## Slide 191: Operation Validation
Operation Validation
  During this period, the 30-day testing period occurs
  As required, fine tuning of the operation and/or design will occur

## Slide 192: Operation Validation
Operation Validation
  All design package submissions are updated and As-Built (Record) plans are submitted
    Upon completion of the 30‑day test, a 180-day warranty period begins for the contractor to guarantee the in-service operation of mechanical and electrical equipment, related components, and the controller assembly

## Slide 193: Traffic Signal Inspection Form
Draft Inspection Form
  Click on Player Attachments above to download
Manual Section 6.12

## Slide 194: Module 6 Completion
You have now completed module 6
To review any section in this module, use the “Outline” on the left
Exam
  Necessary to receive credit for course
  70% required to pass
  Instructions at the start of the exam
  Exam is timed (30 minutes)
  Return to Training Calendar or use instructions that have been provided
Notes: Module 6,